## Slide 1
<Partner logo>
Principles
Extra Information For Teachers
Content created by
Last updated 18th October 2019

## Slide 2
A fuel cell is a device that converts the chemical energy from a fuel into electricity through a chemical reaction of positively charged hydrogen ions with oxygen or another oxidizing agent.

## Slide 3
Chemical energy storage device
(e.g. lithium ion battery)
Hydrogen fuel cell
Open system
The anode and cathode are typically Pt on Carbon based materials. The reaction occurs at the triple phase boundary where the catalyst, electrolyte and gas meet.
Reactants are externally supplied, no recharging required.
Closed system
Anode and cathode are typically metals.
Reactants are internally consumed, need periodic recharging.
Basic operating principles of both are very similar, but there are several intrinsic differences.
Fuel Cells Vs Batteries

## Slide 4
Hydrogen fuel cell*
Chemical energy is transformed into heat via chemical reaction
Efficiency is limited by the Carnot limit;
Mechanical energy has to be transformed into electricity
Both are open system where fuel (hydrogen) reacts with the oxidant (Air)
Fuel Cells Vs Thermodynamic system
Thermodynamic (combustion) system
Chemical energy is directly transformed into electricity via electrochemical reaction
Efficiency is NOT limited by the Carnot limit;
Electrical energy is directly produced
* Note that there are many types of fuel cells, which require different fuels, electrode materials and operate under varying conditions (temperature etc). The example of the Hydrogen PEM fuel cell is given as it is considered the most viable alternative to fossil fuel based combustion engines within the automotive industry.

## Slide 5
H2 + ½ O2  H2O + Energy
The chemical reaction of a fuel cell is the following:
Anodic reaction: Hydrogen oxidation reaction (HOR):
H2 → 2H+ + 2e−
Cathodic reaction: Oxygen reduction reaction (ORR) (is limiting step reaction within a fuel cell due to its sluggish kinetics):
acidic media
O2 + 4H+ + 4e− → 2H2O direct (4 electron pathway) ,
O2 + 2H+ + 2e− → H2O2 indirect (2 electron pathway) H2O2 + 2H+ + 2e− → 2H2O
Alkaline media
O2 + 2H2O + 4e− → 4OH− direct (4 electron pathway)
O2 + H2O + 2e− → HO2− + OH− indirect (2 electron pathway)
HO2− + H2O + 2e− → 3OH−
The 4 electron is desired as the hydrogen peroxide produced in the 2 electron pathway can cause cell degradation and loss of efficiency. An efficient catalyst is therefore required for the 4 electron pathway to occur. This is typically Pt based.

## Slide 6
ΔHr = ΔGr + T ΔSr
ΔHr : Standard Enthalpy (= total energy) of reaction
ΔGr : Free Gibbs energy(= available electrical energy) of reaction
ΔSr : Entropy (= heat disorder.. ) of reaction
T : Reaction temperature
Thermodynamic main properties are:
Related by the following:

## Slide 7
Thermodynamic properties depend on:
Reacting species
Temperature
Pressure
For hydrogen reaction in fuel cells:
ΔHr at 25°C and 1 bar: 241.61 kJ/mol
ΔSr at 25°C and 1 bar: 43.58 J/mol K
ΔGr at 25°C and 1 bar: 254.61 kJ/mol
H2 + ½ O2  H2O + Energy

## Slide 8
ΔHr = ΔGr + T ΔSr
Note that ΔGr and ΔSr are functions of temperature
H2 + ½ O2  H2O + Energy

## Slide 9
Fuel cells convert chemical energy directly into electrical energy. In the ideal case of an electrochemical converter, such as a fuel cell, the change in Gibbs free energy, ΔG, of the reaction is available as useful electric energy at the temperature of the conversion.
ΔGr = WORK
H2 + ½ O2  H2O + Energy
with work equivalent to charge moved in the electric field (potential) it follows:
ΔGr = n F Er
n = mole of electrons involved in the reactions. For hydrogen n=2
F = Farday constant 96485.3329 C/mol
Er = ideal reaction potential

## Slide 10
Ideal reaction potential in a battery
Cu2+ + 2e− → Cu
Zn → Zn2+ + 2e−
Cu2+ + Zn → Cu + Zn2+
Redox reactions

## Slide 11
Ideal reaction potential in a battery
E0
Cu2+ + 2e− → Cu (E = +0.34 V)
Zn → Zn2+ + 2e− (E = −0.76 V)
Cu2+ + Zn → Cu + Zn2+
E0 =0.34 V −(−0.76 V) = 1.10 V

## Slide 12
Ideal reaction potential in a fuel cell
Er = ΔGr / ( n F )
In standard conditions: E0 = 1.185 V
H2 + ½ O2  H2O + Energy

## Slide 13
Standard reaction potential in a fuel cell
Reaction potential (Er) is function of thermodynamic conditions, like ΔGr
Er decreases when temperature increases

## Slide 14
Nernst low
Reaction potential → Equilibrium potential
The Nernst equation provides a relationship between the ideal standard potential (Er) for the cell reaction and the ideal equilibrium potential (E) at other temperatures and partial pressures of reactants (Preac) and partial pressures of products (Pprod)

## Slide 15
Useful amounts of work (electrical energy) are obtained from a fuel cell only when a reasonably current is drawn, but the actual potential is decreased from its equilibrium potential because of irreversible losses
The losses are called:
Activation Polarization
Ohmic Polarization
Concentration Polarization

## Slide 16
Vcell = Vcathode – Vanode – iR
Cell Voltage
The cell voltage includes the contribution of the anode and cathode potentials and ohmic polarization:
Is possible to define voltage efficiency: as the ratio between cell real voltage (V) and ideal voltage (Er).

## Slide 17
Reactant utilization
It is apparent from the Nernst equation that fuel and oxidant gases containing higher partial pressures of electrochemical reactants produce a higher cell voltage.
To keep high operative voltage not all the hydrogen reacts in the cell and a part of the fuel is vented in the outlet.

## Slide 18
Fuel Utilization factor
Is possible to calculate the utilization of hydrogen and of oxygen as the ratio between reacted species and inlet one.
H2  2e- + 2H+
Reacted species are directly calculated from the current (I).
Since current is defined as the product of electron mole flow and Faraday constant:
And electron mole flow is twice hydrogen involved in the reaction:
Anodic semi-reaction

## Slide 19
Fuel Utilization factor
Is possible to calculate the utilization of hydrogen and of oxygen as the ratio between reacted species and inlet one.

## Slide 20
In general is possible to define cell efficiency as the ratio between outlet power Pout (electrical) and inlet power Pin (fuel energy)

## Slide 21
Is possible to elaborate the equation so to obtain..
.. that fuel cell efficiency depends on reversible efficiency, utilisation of fuel and voltage efficiency.

## Slide 22
In general:
ηrev depends on the type of fuel (in general hydrogen) and on the thermodynamic conditions;
uf is related to the design of the cell;
ηv depends on the performance of the materials and on the quality of contacts;

## Slide 23
Parameter with impact on fuel cell efficiency
  Temperature
  Pressure
  Utilisation of reactants
  Current density
  Impurities/contaminant
  time
Operating conditions are a trade off between operative cost and capital cost.